## Slide 1: Lecture 1
IoT Architecture Lab

## Slide 2: IoT Architecture

## Slide 3: Overview of IoT Architecture
Sensors/Devices: Collection of data from the environment (e.g., temperature sensors, motion detectors, cameras).
Connectivity: Methods for devices to communicate (e.g., Wi-Fi, Bluetooth, Zigbee, LoRaWAN).
Edge Computing: Local processing at the edge devices to reduce latency and bandwidth usage.
Cloud Computing: Centralized data storage, processing, and analysis.
Data Analytics: Tools for analyzing the data collected to derive insights.
User Interface: Dashboard or app for monitoring and interacting with the IoT devices.

## Slide 4: Lab Components
Hardware: Sensors, actuators, microcontrollers (like Arduino, Raspberry Pi), gateways, etc.
Software: Firmware for devices, middleware for data processing, and cloud platforms (like AWS IoT, Azure IoT).
Connectivity Protocols: Testing different protocols like MQTT, CoAP, HTTP/HTTPS, etc.
Security: Implementing and testing encryption, authentication, and other security measures.
Simulation Tools: Tools to simulate IoT environments (e.g., Cisco Packet Tracer, Cooja).

## Slide 5: Lab Exercises
Device Integration: Setting up and integrating different IoT devices.
Data Collection and Processing: Capturing data from sensors, processing it at the edge, and sending it to the cloud.
Real-time Monitoring: Setting up dashboards to monitor data in real-time.
Automation and Control: Implementing automation scenarios where data triggers specific actions (e.g., turning on lights when motion is detected).
Security Implementation: Encrypting communication, implementing secure boot, and setting up secure device management.
Performance Testing: Evaluating the performance of the IoT system under different loads.

## Slide 6: Tools and Platforms
Development Kits: ESP32, Raspberry Pi, Arduino.
Cloud Platforms: AWS IoT Core, Google Cloud IoT, Azure IoT Hub.
Data Analytics Tools: MATLAB, Python libraries (Pandas, NumPy), IoT analytics platforms.
Simulation and Visualization: MATLAB Simulink, Node-RED, Grafana for dashboards.

## Slide 7: Modern Application of IoT
Smart Grids and energy saving
Smart cities
Smart homes/Home automation
Healthcare
Earthquake detection
Radiation detection/hazardous gas detection
Smartphone detection
Water flow monitoring
Traffic monitoring
Smart door lock protection system
Robots and Drones
Healthcare and Hospitals, Telemedicine applications
Biochip Transponders (For animals in farms)
Heart monitoring implants (Example Pacemaker, ECG real time tracking)

## Slide 8: What is Arduino?
An Arduino board consists of an Atmel 8-bit AVR microcontroller with complementary components that facilitate programming and incorporation into other circuits.
It's an open-source physical computing platform based on a simple microcontroller board, and a development environment for writing software for the board

## Slide 9: What is Arduino?

## Slide 10: Why Arduino
Open source and extensible software- The Arduino software is published as open source tools, available for extension by experienced programmers. The language can be expanded through C++ libraries
Open source and extensible hardware -The Arduino is based on Atmel's ATMEGA8 and ATMEGA168 microcontrollers. The plans for the modules are published under a Creative Commons license, so experienced circuit designers can make their own version of the module, extending it and improving it.
Inexpensive
Cross-platform
Simple, clear programming environment

## Slide 11: Arduino UNO board

## Slide 12: UNO Spec

## Slide 13: Arduino has
Flash memory: it's a rewritable non-volatile memory. This means that its content will still be there if you turn off the power. It's a bit like the hard disk on the Arduino board. Your program is stored here. code for writing and retrieving any data structure to EEPROM easily.
RAM: it's like the RAM in your computer. Its content disappears when you turn off the power, but it can be read and written really fast. Every normal variable in your sketch is held in RAM while your sketch runs.
EEPROM: it's an older technology to implement rewritable non-volatile memory. It's normally used to store settings and other parameters between resets.

## Slide 14: Power
The Arduino Uno can be powered via the USB connection or with an external power supply. The power source is selected automatically.
External (non-USB) power can come either from an AC-toDC adapter (wall-wart) or battery. The adapter can be connected by plugging a 2.1mm center-positive plug into the board's power jack. Leads from a battery can be inserted in the Gnd and Vin pin headers of the POWER connector.
The board can operate on an external supply of 6 to 20 volts. If supplied with less than 7V, however, the 5V pin may supply less than five volts and the board may be unstable. If using more than 12V, the voltage regulator may overheat and damage the board. The recommended range is 7 to 12 volts

## Slide 15: Arduino Nano V3.0

## Slide 16: Arduino Mega

## Slide 17: Getting Started !
Visit: http://arduino.cc/en/Main/Software
Download & install the Arduino environment (IDE) for Windows, Mac, or Linux. (Latest version: 1.6)
Launch the Arduino IDE
Select your board (Tools>>board>>UNO)
Select Port No

## Slide 18: Arduino IDE

## Slide 20: Our First Program ! Blink
Now, you will learn how to make the built-in LED blink

## Slide 21: Our First Program ! Blink
You might notice that your Arduino board's built-in LED already blinks when you connect it to a USB.
This is because Arduino boards are generally shipped with the 'Blink' sketch preinstalled.
We will do a simple variation to the program by changing the rate of the blink

## Slide 22: Our First Program ! Blink

## Slide 23: Understand the code

## Slide 24: Run the code
Make sure that Arduino is connected to your PC.
Click Upload and wait until the status is done.

## Slide 25: Ex1-Blink using External LED
Connect a LED to any digital pin on your Arduino, and put a resistance (270 ohm) in series to limit the current passing through the LED.
Make the necessary code changes.
Change the resistance value: 470 ohm, 1K, 10K, What is your observation?
Observation: The LED illumination decreases as larger resistance is used.

## Slide 26: Ex1-Blink using External LED

## Slide 27: Ex2-LEDs Traffic

## Slide 28: Ex2-LEDs Traffic

## Slide 29
Thank You